## Slide 1
Routing Algorithm
Prof. Liu Liang
EIE4113 Wireless and Mobile Systems
Week 6

## Slide 2: Routing is Necessary for Wireless Network
When the transmitter and receiver are not in the same cell, base stations should talk with each other
  Base stations are connected by fiber cables (backhaul network)

## Slide 3: Routing is Necessary for Wireless Network
When you are at Hong Kong, and your friend is at London
  Your signal is sent to a base station
  Signal is then routed to London, and then a base station there serves your friend

## Slide 4: Routing in Fiber Network
When transmitter and receiver is connected via a lot of routers, it is hard to find a good routing strategy

## Slide 5: Routing in Fiber Network
When transmitter and receiver is connected via a lot of routers, it is hard to find a good routing strategy

## Slide 6: IP Address
IP addresses are 32-bit long, usually expressed in the dotted-decimal notation A.B.C.D
Example: 152.123.1.2
10011000 10000100 00000001 00000010

## Slide 7: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets traverse from given initial source host to final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical

## Slide 8: Routing tables
Within each router, there is a routing table specifying how to route packets to the destination.
The rules that used to build a routing table is called a routing algorithm.
Example:
  Destination: IP address of final destination
  Outgoing interface: index
  Gateway: IP address of next hop
Destination (IP) | Gateway (IP) | Interface (Index)
A
B
C
1 2 3 4
1 2 3 4
1 2 3 4
IP of Network B
1
IP of B’s Interface 4
IP of Network C
2
IP of C’s Interface 1
Each interface: 1 IP address

## Slide 9: Routing example
Two networks are connected through three routers
A
158.132.148.111
B
158.147.103.222
158.147.0.1
158.132.0.1
Interface 1
Interface 2
Interface 1
Interface 3
Interface 7
Interface 4
154.207.0.2
154.207.0.3
154.207.0.1
154.207.0.5

## Slide 10: Routing example
Routing table at each router
Network Destination | Gateway | Interface
158.147.0.0 | 154.207.0.1 | 2
158.132.0.0 | Directly | 1
Network Destination | Gateway | Interface
158.147.0.0 | 154.207.0.3 | 3
158.132.0.0 | 154.207.0.2 | 1
Network Destination | Gateway | Interface
158.147.0.0 | Directly | 4
158.132.0.0 | 154.207.0.5 | 7
A
158.132.148.111
B
158.147.103.222
158.147.0.1
158.132.0.1
Interface 1
Interface 2
Interface 1
Interface 3
Interface 7
Interface 4
154.207.0.2
154.207.0.3
154.207.0.1
154.207.0.5

## Slide 11: Routing example
Host A to Host B - IP and Ethernet Addresses
Destination IP: 158.147.103.222
Ethernet Frame
Network Destination | Gateway | Interface
158.147.0.0 | 154.207.0.1 | 2
158.132.0.0 | Directly | 1
A
158.132.148.111
B
158.147.103.222
158.147.0.1
158.132.0.1
Interface 1
Interface 2
Interface 1
Interface 3
Interface 7
Interface 4
154.207.0.2
154.207.0.3
154.207.0.1
154.207.0.5

## Slide 12: Routing example
Host A to Host B (cont’d) - IP and Ethernet Addresses
Destination IP: 158.147.103.222
Ethernet Frame
Network Destination | Gateway | Interface
158.147.0.0 | 154.207.0.3 | 3
158.132.0.0 | 154.207.0.2 | 1
A
158.132.148.111
B
158.147.103.222
158.147.0.1
158.132.0.1
Interface 1
Interface 2
Interface 1
Interface 3
Interface 7
Interface 4
154.207.0.2
154.207.0.3
154.207.0.1
154.207.0.5

## Slide 13: Routing example
Host A to Host B (cont’d) - IP and Ethernet Addresses
Destination IP: 158.147.103.222
Ethernet Frame
Network Destination | Gateway | Interface
158.147.0.0 | Directly | 4
158.132.0.0 | 154.207.0.5 | 7
A
158.132.148.111
B
158.147.103.222
158.147.0.1
158.132.0.1
Interface 1
Interface 2
Interface 1
Interface 3
Interface 7
Interface 4
154.207.0.2
154.207.0.3
154.207.0.1
154.207.0.5

## Slide 14: Routing example
Host A to Host B (cont’d) - IP and Ethernet Addresses
Destination IP: 158.147.103.222
Ethernet Frame
A
158.132.148.111
B
158.147.103.222
158.147.0.1
158.132.0.1
Interface 1
Interface 2
Interface 1
Interface 3
Interface 7
Interface 4
154.207.0.2
154.207.0.3
154.207.0.1
154.207.0.5

## Slide 15: Graph abstraction: link costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
ca,b: cost of direct link connecting a and b
e.g., cw,z = 5, cu,z = ∞
  cost defined by network operator: could always be 1, or inversely related to bandwidth, or related to congestion
N (node): set of routers = { u, v, w, x, y, z }
E (edge): set of links ={ (u,v), (u,x), (u,w), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }

## Slide 16: Dijkstra’s link-state routing algorithm
centralized: network topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (“source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k destinations
ca,b: direct link cost from node a to b; = ∞ if not direct neighbors
D(b): current estimate of cost of least-cost-path from source to destination b
p(b): predecessor node along path from source to b
N': set of nodes whose least-cost-path definitively known
notation

## Slide 17: Dijkstra’s link-state routing algorithm
1 Initialization:
2 N' = {u} /* compute least cost path from u to all other nodes */
3 for all nodes b
4 if b adjacent to u /* u initially knows direct-path-cost only to direct neighbors */
5 then D(b) = cu,b /* but may not be minimum cost! */
6 else D(b) = ∞
7
8 Loop
9
10
11
12
13
14
15 until all nodes in N'
find a not in N' such that D(a) is a minimum
add a to N'
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
/* new least-path-cost to b is either old least-cost-path to b or known
least-cost-path to a plus direct-cost from a to b */

## Slide 18: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
4,y
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
4,y
3,y
5,u
∞
∞
1,u
2,u
∞
2,x
4,x
2,u
4,y
3,y
2,u
uxyvwz
uxyvw
uxyv
uxy
ux
u
v
w
x
y
z
find a not in N' such that D(a) is a minimum
add a to N'
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
Initialization (step 0): For all a: if a adjacent to then D(a) = cu,a
one-hop cost
why?
Is it possible to visit v, w, y, or z with lower cost in two hops via x?
one-hop and two-hop cost
Other than u and x, the one-hop and two-hop costs to other routers are always equal to or larger than 2 (the minimum one-hop and two-hop cost). Hence, it is not possible to find better path to y via the other routers.

## Slide 19: Dijkstra’s algorithm: an example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
4,x
3,y
3,y
u
y
x
w
v
z
resulting least-cost-path tree from u:
resulting forwarding table in u:
v
x
y
w
x
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
outgoing link
route from u to v directly
route from u to all other destinations via x

## Slide 20: Dijkstra’s algorithm: another example
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v),
p(v)
0
1
2
3
4
5
D(w),
p(w)
D(x),
p(x)
D(y),
p(y)
D(z),
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct least-cost-path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz
v
w
x
y
z

## Slide 21: Dijkstra’s algorithm: discussion
algorithm complexity: n nodes
each of n iteration: need to check all nodes, b, not in N’
n(n+1)/2 comparisons: O(n2) complexity
more efficient implementations possible: O(nlogn)
message complexity:
each router must broadcast its link state information to other n routers
efficient (and interesting!) broadcast algorithms: O(n) link crossings to disseminate a broadcast message from one source
each router’s message crosses O(n) links: overall message complexity: O(n2)

## Slide 22: Mid-Term Test
Mid-Term Test: 10%
  Time: Wednesday of Week 7, 9:50 – 11:20
  Location: HJ202
  Closed-book exam
  Week 1 – Week 6